| Not To Scale |
| --- |
| Site: Lat/Long: | Waste Water Treatment Plant East 283008/811144 | SJRWMD |
| Project No: | 31-58200 | Figure 1. Site Map |

| Site: | Waste Water Treatment Plant East | SJRWMD |
| --- | --- | --- |
| Well Completed: | September 16, 1998 | Figure 4. Floridan Monitor WellOR-0668 |

Table 7.				Grout Data			(page 1 of 3)

Site:Waste Water Treatment Plant    			Well Number: OR-0668 (Floridan)

| DATE | TAG DEPTH (ft) | ANNULUS/ BORE (in.) | VOLUME (yds/bgs) | MATERIAL | COMMENTS |
| --- | --- | --- | --- | --- | --- |
| 1/26/98 | 34 | A-36 | 31 bgs | Grout | Grout 34 ft of 30 in. dia. steel casing |
| 1/27/98 | 20 | A-36 | 27 bgs | Grout | Grout 30 in. dia. steel casing to surface |
| 2/5/98 | 125 | A-29 | 222 bgs | Grout | Pressure grout 125 ft of 24 in. dia. steel casing |
| 2/7/98 | 20 | A-29 | NA | NA | Grout annulus at a later date |
| 2/11/98 | 202 | A-23 | 235 bgs | Grout | Pressure grout 197 ft of 18 in. dia. steel casing |
| 2/12/98 | 30 | A-23 | 31 bgs | Grout | Tremie grout 18 in. dia. steel casing to land surface |
| 2/12/98 | 20 | A-29 | 24 bgs | Grout | Tremie grout 24 in. dia. steel casing to land surface |
| 2/24/98 | 436 | B-18 | 64 bgs | Grout | Backplug dredging zone |
| 2/25/98 | 431 | B-18 | 156 bgs | Grout | Backplug dredging zone; Bore advanced with 8 in. bit ( 431 ft to 467 ft) |
| 2/26/98 | 436 | B-8 | NA | NA | Tag on bore, dredge to 456 ft |
| 2/26/98 | 456 | B-8 | 235 bgs | Grout | Backplug dredging zone |
| 3/2/98 | 438 | B-8 | NA | NA | Tag on bore, drill with 17 in. bit |
| 3/12/98 | 602 | A-18 | 194 bgs | Grout | Pressure grout 602 ft of 12 in. dia. steel casing |
| 3/13/98 | 543 | A-18 | 216 bgs | Grout | Tremie grout 12 in. dia. steel casing |
| 3/16/98 | 458 | A-18 | 209 bgs | *Grout/ Blended | Tremie grout 12 in. dia. steel casing |
| 3/18/98 | 457 | A-18 | 10 yds | Gravel | Gravel used to fill voids |
| 3/19/98 | 457 | A-18 | 35 yds | Gravel | Gravel used to fill voids |
| 3/20/98 | 436 | A-18 | 30 yds | Gravel | Gravel used to fill voids |
| 3/20/98 | 326 | A-18 | 26 bgs | *Grout/ Blended | Tremie grout 12 in. dia. |

*Grout/Blended: Neat cement mixed with 12% bentonite and durafiber

Table 7.				Grout Data			(page 2 of 3)

Site:Waste Water Treatment Plant    			Well Number: OR-0668 (Floridan)

| DATE | TAG DEPTH (ft) | ANNULUS/ BORE (in.) | QUANITY (yds/bgs) | MATERIAL | COMMENTS |
| --- | --- | --- | --- | --- | --- |
| 3/21/98 | 316 | A-18 | 100 bgs | *Grout/ Blended | Tremie grout 12 in. dia. steel casing |
| 3/23/98 | 253 | A-18 | 6 yds | Gravel | Gravel used to fill voids |
| 3/23/98 | 205 | A-18 | 24 bgs | Grout | Tremie grout |
| 3/24/98 | 200 | A-18 | 110 bgs | Grout | Tremie grout |
| 3/27/98 | 40 | A-18 | NA | NA | Grouting finished 8/14/98 |
| 7/23/98 | 1490 | B-12 | NA | NA | Place 1,490 ft of 6 in. dia. SDR 17 well casing in bore |
| 7/23/98 | 1490 | A-12 | 10 bgs | Hole plug | Pour hole plug to the 3 catch baskets located near the bottom of the well casing |
| 7/24/98 | no tag | A-12 | 15 bgs | Grout | Grout tremied |
| 7/28/98 am | 1471 | A-12 | 50 bgs | Grout | Grout tremied |
| 7/28/98 pm | 1440 | A-12 | 100 bgs | Grout | Grout tremied |
| 7/29/98 | 1365 | A-12 | 100 bgs | Grout | Grout tremied |
| 7/30/98 | 1358 | A-12 | 100 bgs | Grout | Grout tremied |
| 7/31/98 | 1350 | A-12 | 100 bgs | Grout | Grout tremied |
| 8/3/98 | 1334 | A-12 | 5 yds | Gravel | Gravel used to fill voids |
| 8/4/98 | 1200 | A-12 | 5 yds | Gravel | Gravel used to fill voids |
| 8/4/98 | 1095 | A-12 | 25 bgs | Grout | Grout tremied |
| 8/5/98 | 1061 | A-12 | 100 bgs | Grout | Grout tremied |
| 8/6/98 am | 987 | A-12 | 100 bgs | Grout | Grout tremied |
| 8/6/98 pm | 903 | A-12 | 100 bgs | Grout | Grout tremied |
| 8/7/98 | 817 | A-12 | 100 bgs | Grout | Grout tremied |
| 8/10/98 | 790 | A-12 | NA | NA | Order gravel |
| 8/11/98 | 790 | A-12 | 10 yds | Gravel | Gravel used to fill voids |
| 8/11/98 | 685 | A-12 | 25 bgs | Grout | Grout tremied |
| 8/12/98 am | 640 | A-12 | 100 bgs | Grout | Grout tremied; water return from annulus |
| 8/13/98 am | 399 | A-12 | 100 bgs | Grout | Grout tremied |
| 8/13/98 pm | 176 | A-12 | 64 bgs | Grout | Grout tremied with return |
| 8/14/98 | 10 | A-12 | 5 bgs | Grout | Casing grouted to land surface |
| 8/14/98 | 40 | A-18 | 20 bgs | Grout | Casing grouted to land surface |

*Grout/Blended: Neat cement mixed with 12% bentonite and durafiber

Table 7.				Grout Data			(page 3 of 3)

Site:Waste Water Treatment Plant    			Well Number: OR-0668 (Floridan)

| DATE | TAG DEPTH (ft) | ANNULUS/ BORE (in.) | QUANITY (yds/bgs) | MATERIAL | COMMENTS |
| --- | --- | --- | --- | --- | --- |
| 8/17/98 | 2498 | B-12 | 235 bgs | Grout | Backplug; grout sets up on tremie pipe at 2,245 ft, Tremie pipe breaks at 300 ft while attempting to free pipe from grout |
| 9/3/98 | 1780 | B-12 | NA | NA | Cut off and retrieve tremie pipe; leave 465 ft of tremie pipe in bore |
| 9/9/98 | No tag | B-12 | 150 bgs | Grout | Backplug |
| 9/10/98 | 2090 | B-12 | 14 yds | Pea-gravel | Fill large voids |
| 9/10/98 | 1960 | B-12 | 25 bgs | Grout | Backplug |
| 9/11/98 | 1920 | B-12 | 150 bgs | Grout | Backplug |
| 9/14/98 am | 1875 | B-12 | 6 yds | Pea-gravel | Fill large voids |
| 9/14/98 am | 1835 | B-12 | 25 bgs | Grout | Backplug |
| 9/14/98 pm | 1790 | B-12 | 100 bgs | Grout | Backplug |
| 9/15/98 am | 1690 | B-12 | 100 bgs | Grout | Backplug |
| 9/15/98 pm | 1620 | B-12 | 60 bgs | Grout | Backplug |
| 9/16/98 | 1537 | B-12 | NA | NA | Final tag, grouting complete |

*Grout/Blended: Neat cement mixed with 12% bentonite and durafiber

Table 1.			Groundwater Levels 		(page 1 of 3)

Site: Waste Water Treatment Plant	                               Well ID: OR-0668 (Floridan)

| Water Levels | Borehole |
| --- | --- |
| Date/Time (yy:mm:dd/hh:mm) | Casing (ft, bls) | Rod (ft, bls) | Total Depth (ft, bls) | Open Hole (ft) |
| 980218/1015 | 39.0 | 39.0 | 250 | 53 |
| 980218/1425 | 39.0 | 38.9 | 280 | 83 |
| 980218/1605 | 39.0 | 39.1 | 311 | 114 |
| 980218/1750 | 39.1 | 38.9 | 342 | 145 |
| 980218/1900 | 38.9 | 38.3 | 374 | 177 |
| 980219/1130 | 39.0 | 39.3 | 404 | 207 |
| 980223/1055 | 38.3 | 38.5 | 436 | 239 |
| 980303/1335 | 38.1 | 37.8 | 471 | 274 |
| 980303/1745 | 39.6 | 39.2 | 503 | 306 |
| 980304/1530 | 39 | NR | 534 | 337 |
| 980306/0830 | 39.3 | 39.3 | 565 | 368 |
| 980306/1230 | 39.3 | 39.4 | 596 | 399 |
| 980306/1430 | 39.5 | 39.4 | 608 | 411 |
| 980327/0925 | 41.0 | 41.7 | 655 | 51 |
| 980327/1110 | 41.0 | 41.5 | 687 | 83 |
| 980327/1340 | 41.3 | 41.4 | 718 | 114 |
| 980327/1525 | 41.4 | 41.6 | 749 | 145 |
| 980331/1020 | 41.5 | 41.4 | 780 | 176 |
| 980331/1300 | 41.5 | 41.7 | 811 | 207 |
| 980331/1500 | 41.5 | 41.5 | 842 | 238 |
| 980331/1725 | 41.5 | 41.5 | 872 | 268 |
| 980331/1900 | 41.6 | 42.5 | 901 | 297 |
| 980401/1040 | 41.6 | 41.7 | 930 | 326 |
| 980401/1215 | 41.6 | 41.8 | 962 | 358 |
| 980401/1350 | 41.4 | 41.8 | 992 | 388 |
| 980401/1550 | 41.4 | 41.7 | 1025 | 421 |
| 980401/1900 | 41.3 | 41.9 | 1055 | 451 |
| 980402/1115 | 41.5 | 41.5 | 1086 | 482 |
| 980402/1510 | 41.5 | 41.7 | 1118 | 514 |
| 980402/1755 | 41.4 | 41.6 | 1148 | 544 |

Table 1.			Groundwater Levels 		(page 2 of 3)

Site: Waste Water Treatment Plant	                               Well ID: OR-0668 (Floridan)

| Water Levels | Borehole |
| --- | --- |
| Date/Time (yy:mm:dd/hh:mm) | Casing (ft, bls) | Rod (ft, bls) | Total Depth (ft, bls) | Open Hole (ft) |
| 980403/1240 | 41.6 | 41.6 | 1179 | 575 |
| 980403/1400 | 41.8 | 43.3 | 1190 | 586 |
| 980406/1140 | 42.1 | 42.2 | 1210 | 606 |
| 980406/1515 | 41.8 | 42.1 | 1241 | 637 |
| 980406/1820 | 41.7 | 42.0 | 1271 | 667 |
| 980406/1900 | 41.7 | NR | 1302 | 698 |
| 980407/1115 | 41.8 | 42.2 | 1332 | 728 |
| 980407/1620 | 41.9 | 42.6 | 1364 | 760 |
| 980407/2030 | 41.8 | 41.9 | 1395 | 791 |
| 980427-1615 | 44.6 | 45.9 | 1430 | 826 |
| 980428-0919 | 45.0 | 47.3 | 1461 | 857 |
| 980428-1245 | 44.8 | 48.0 | 1492 | 888 |
| 980428-1830 | 43.8 | 53.2 | 1523 | 919 |
| 980428-2200 | 44.0 | 50.9 | 1554 | 950 |
| 980429-0900 | 46.1 | 55.8 | 1554 | 950 |
| 980429-1234 | 44.9 | 49.4 | 1584 | 980 |
| 980429-1900 | 44.9 | 54.4 | 1617 | 1013 |
| 980429-2230 | 44.8 | 56.7 | 1648 | 1044 |
| 980430-1420 | 40.8 | 55.8 | 1685 | 1081 |
| 980430-NR | 45.4 | 57.9 | 1712 | 1108 |
| 980501-1255 | 44.3 | 56.7 | 1743 | 1139 |
| 980505-1800 | 44.4 | 56.7 | 1775 | 1171 |
| 980506-1340 | 45.2 | 56.6 | 1808 | 1204 |
| 980506-1723 | 44.6 | 57.4 | 1839 | 1235 |
| 980506-1930 | 45.9 | 57.8 | 1870 | 1266 |
| 980507-1745 | 45.2 | 79.6 | 1900 | 1296 |
| 980507-2100 | 44.7 | 78.4 | 1905 | 1301 |
| 980511-1656 | 44.5 | 83.2 | 1933 | 1329 |
| 980511-1900 | 44.7 | 84.1 | 1950 | 1346 |
| 980512-1455 | 44.9 | 74.9 | 1965 | 1361 |

Table 1.			Groundwater Levels 		(page 3 of 3)

Site: Waste Water Treatment Plant	                               Well ID: OR-0668 (Floridan)

| Water Levels | Borehole |
| --- | --- |
| Date/Time (yy:mm:dd/hh:mm) | Casing (ft, bls) | Rod (ft, bls) | Total Depth (ft, bls) | Open Hole (ft) |
| 980512-0930 | 51.0 | 82.6 | 1995 | 1391 |
| 980513-1645 | 45.0 | 70.7 | 2027 | 1423 |
| 980513-2000 | 44.8 | 83.1 | 2048 | 1444 |
| 980514-1200 | 45.2 | 77.6 | 2089 | 1485 |
| 980514-2000 | 46.3 | 79.0 | 2100 | 1496 |
| 980515-1400 | 46.1 | 78.2 | 2120 | 1516 |
| 980518-1500 | 44.7 | 71.5 | 2150 | 1546 |
| 980518-2000 | 45.5 | 71.7 | 2183 | 1579 |
| 980519-1305 | 45.9 | 70.5 | 2215 | 1611 |
| 980519-2000 | 46.4 | 73.3 | 2235 | 1631 |
| 980520-1100 | 45.9 | 70.3 | 2247 | 1643 |
| 980520-2000 | 45.6 | 70.2 | 2279 | 1675 |
| 980521-1050 | 45.0 | 70.1 | 2310 | 1706 |
| 980521-1440 | 45.8 | 70.0 | 2341 | 1737 |
| 980521-2100 | 45.8 | 71.6 | 2373 | 1769 |
| 980522-1700 | 46.4 | 70.5 | 2403 | 1799 |
| 980526-1900 | 45.5 | 72.4 | 2434 | 1830 |
| 980603-2000 | 47.1 | 74.4 | 2465 | 1861 |
| 980603-2200 | 46.8 | 79.0 | 2498 | 1894 |

Table 2.                     		 	Drilling Data			(page 1 of  2)

Site: Waste Water Treatment Plant			Well ID: OR-0668 (Floridan)

| From (ft, bls) | To (ft, bls) | Bit Size (in.) | Time (min) | Rate (ft/hr) |
| --- | --- | --- | --- | --- |
| 250 | 280 | 17 | 200 | 9 |
| 280 | 311 | 17 | 60 | 31 |
| 311 | 342 | 17 | 62 | 30 |
| 342 | 374 | 17 | 38 | 51 |
| 374 | 404 | 17 | 107 | 17 |
| 404 | 432 | 17 | 127 | 13 |
| 432 | 434 | 17 | Dredge | NA |
| 434 | 471 | 17 | Dredge | NA |
| 471 | 503 | 17 | 246 | 8 |
| 503 | 534 | 17 | 388 | 5 |
| 534 | 565 | 17 | 443 | 4 |
| 565 | 596 | 17 | 172 | 11 |
| 596 | 608 | 17 | 50 | 14 |
| 608 | 655 | 117/8 | NR | NA |
| 655 | 687 | 117/8 | 80 | 24 |
| 687 | 718 | 117/8 | 100 | 19 |
| 718 | 749 | 117/8 | 76 | 24 |
| 749 | 780 | 117/8 | 103 | 18 |
| 780 | 811 | 117/8 | 103 | 18 |
| 811 | 842 | 117/8 | 91 | 20 |
| 842 | 872 | 117/8 | 115 | 16 |
| 872 | 901 | 117/8 | 91 | 19 |
| 901 | 930 | 117/8 | 81 | 21 |
| 930 | 962 | 117/8 | 60 | 32 |
| 962 | 992 | 117/8 | 79 | 23 |
| 992 | 1025 | 117/8 | 94 | 21 |
| 1025 | 1055 | 117/8 | 200 | 9 |
| 1055 | 1086 | 117/8 | 124 | 15 |
| 1086 | 1118 | 117/8 | 213 | 9 |
| 1118 | 1148 | 117/8 | 143 | 13 |
| 1148 | 1179 | 117/8 | 239 | 8 |
| 1179 | 1210 | 117/8 | 239 | 8 |
| 1210 | 1241 | 117/8 | 172 | 11 |
| 1241 | 1271 | 117/8 | 143 | 13 |
| 1271 | 1302 | 117/8 | 91 | 20 |
| 1302 | 1332 | 117/8 | 130 | 14 |
| 1332 | 1364 | 117/8 | 290 | 7 |

Table 2.                     			 Drilling Data		(page 2 of  2)

Site: Waste Water Treatment Plant			Well ID: OR-0668 (Floridan)

| From (ft, bls) | To (ft, bls) | Bit Size (in.) | Time (min) | Rate (ft/hr) |
| --- | --- | --- | --- | --- |
| 1332 | 1364 | 117/8 | 290 | 7 |
| 1364 | 1395 | 117/8 | 194 | 10 |
| 1430 | 1461 | 117/8 | 194 | 10 |
| 1461 | 1492 | 117/8 | 155 | 12 |
| 1492 | 1523 | 117/8 | 182 | 10 |
| 1523 | 1554 | 117/8 | 194 | 10 |
| 1554 | 1554 | 117/8 | NA | NA |
| 1554 | 1584 | 117/8 | 188 | 10 |
| 1584 | 1617 | 117/8 | 182 | 11 |
| 1617 | 1648 | 117/8 | 194 | 10 |
| 1648 | 1680 | 117/8 | 246 | 8 |
| 1680 | 1712 | 117/8 | NR | NA |
| 1712 | 1743 | 117/8 | 239 | 8 |
| 1743 | 1775 | 117/8 | 320 | 6 |
| 1775 | 1808 | 117/8 | 330 | 6 |
| 1808 | 1839 | 117/8 | 141 | 13 |
| 1839 | 1870 | 117/8 | 119 | 16 |
| 1870 | 1900 | 117/8 | 600 | 3 |
| 1900 | 1933 | 117/8 | NR | NA |
| 1933 | 1965 | 117/8 | NR | NA |
| 1965 | 1995 | 117/8 | 375 | 5 |
| 1995 | 2027 | 117/8 | 400 | 5 |
| 2027 | 2058 | 117/8 | 517 | 4 |
| 2058 | 2089 | 117/8 | 310 | 6 |
| 2089 | 2120 | 117/8 | 231 | 8 |
| 2120 | 2150 | 117/8 | 231 | 8 |
| 2150 | 2183 | 117/8 | 254 | 8 |
| 2183 | 2215 | 117/8 | 246 | 8 |
| 2215 | 2247 | 117/8 | 267 | 7 |
| 2247 | 2279 | 117/8 | 267 | 7 |
| 2279 | 2310 | 117/8 | 194 | 10 |
| 2310 | 2341 | 117/8 | 194 | 10 |
| 2341 | 2373 | 117/8 | 246 | 8 |
| 2373 | 2403 | 117/8 | 429 | 4 |
| 2403 | 2433 | 117/8 | 429 | 4 |
| 2433 | 2465 | 117/8 | 640 | 3 |
| 2465 | 2498 | 117/8 | 660 | 3 |

Table 4.			Groundwater Quality    		(page 1 of  3)

Site:Waste Water Treatment Plant    			Well Number: OR-0668 (Floridan)

Hydrologist: RBrooks	                                                Casing Depth: 1490 ft

| LAB ( | Date/Time (yy:mm:dd/hh:mm) | Sample Depth (ft, bls) | Open Hole (ft) | Temp (Deg C) | Chlorides (mg/L) | Conductivity (us/cm) |
| --- | --- | --- | --- | --- | --- | --- |
| ( | 980218/1015 | 250 | 53 | 23 | 18.4 | 368 |
|  | 980218/1405 | 280 | 83 | 24 | 5.9 | 386 |
|  | 980218/1540 | 311 | 114 | 24 | 7.0 | 376 |
|  | 980218/1735 | 342 | 145 | 23 | 8.5 | 385 |
|  | 980218/1850 | 374 | 177 | 23 | 10 | 373 |
|  | 980219/1120 | 404 | 207 | 23 | 11.8 | 393 |
|  | 980223/1040 | 436 | 239 | 23.5 | 8.9 | 355 |
|  | 980303/1105 | 471 | 274 | 23 | 19.2 | 269 |
|  | 980304/0730 | 503 | 306 | 23 | 15 | 296 |
|  | 980304/1440 | 534 | 337 | 24 | 11.5 | 287 |
|  | 980306/0820 | 565 | 368 | 23.5 | 14.8 | 298 |
|  | 980306/1140 | 596 | 399 | 24 | 10 | 288 |
|  | 980306/1415 | 608 | 411 | 24 | 10 | 295 |
|  | 980327/0750 | 655 | 51 | 24 | 17.4 | 359 |
|  | 980327/1100 | 687 | 83 | 25 | 18.6 | 361 |
|  | 980327/1340 | 718 | 114 | 25 | 18.6 | 381 |
|  | 980327/1515 | 749 | 145 | 25 | 18.4 | 381 |
|  | 980331/1000 | 780 | 176 | 25 | 18.0 | 379 |
|  | 980331/1245 | 811 | 207 | 25 | 17.6 | 376 |
|  | 980331/1450 | 842 | 238 | 25 | 17.8 | 376 |
|  | 980331/1710 | 872 | 268 | 25 | 17.5 | 373 |
|  | 980401/0855 | 901 | 297 | 25 | 11.5 | 352 |
|  | 980401/1030 | 930 | 326 | 25 | 14.8 | 361 |

Table 4.			Groundwater Quality    		(page 2 of  3)

Site:Waste Water Treatment Plant    			Well Number: OR-0668 (Floridan)

Hydrologist: RBrooks	                                                Casing Depth: 1490 ft

| LAB ( | Date/Time (yy:mm:dd/hh:mm) | Sample Depth (ft, bls) | Open Hole (ft) | Temp (Deg C) | Chlorides (mg/L) | Conductivity (us/cm) |
| --- | --- | --- | --- | --- | --- | --- |
|  | 980401/1200 | 962 | 358 | 25 | 14.5 | 371 |
|  | 980401/1345 | 992 | 388 | 25 | 14.8 | 374 |
|  | 980401/1545 | 1025 | 421 | 25 | 15.2 | 373 |
|  | 980402/0730 | 1055 | 451 | 25 | 10 | 351 |
|  | 980402/0955 | 1086 | 482 | 25 | 17 | 371 |
|  | 980402/1415 | 1118 | 514 | 25 | 10 | 381 |
|  | 980402/1750 | 1148 | 544 | 25 | 14.5 | 381 |
|  | 980403/1215 | 1179 | 575 | 25 | 14.9 | 381 |
|  | 980406/1130 | 1210 | 606 | 25 | 23 | 412 |
|  | 980406/1450 | 1241 | 637 | 25 | 29.7 | 443 |
|  | 980406/1805 | 1271 | 667 | 25 | 29.0 | 443 |
|  | 980407/0825 | 1301 | 697 | 25 | 17.8 | 389 |
|  | 980407/1100 | 1332 | 728 | 25 | 52 | 567 |
| ( | 980407/1610 | 1364 | 760 | 25 | 356 | 1883 |
|  | 980408/0745 | 1395 | 791 | 25 | 494 | 2142 |
|  | 980427-1952 | 1461 | 857 | 24.5 | 286 | 1300 |
| ( | 980428-1225 | 1492 | 888 | 26 | 1556 | 5048 |
| ( | 980428-1725 | 1523 | 919 | 26 | 5090 | 14847 |
|  | 980429-0825 | 1554 | 950 | 29 | 5980 | 17655 |
|  | 980429-1225 | 1584 | 980 | 26 | 2680 | 8908 |
|  | 980429-1808 | 1617 | 1013 | 25.5 | 4860 | 11999 |
|  | 980430-NA | 1648 | 1044 | NR | 6400 | 16000 |
|  | 980430-1227 | 1685 | 1081 | 26.5 | 5680 | 14987 |

Table 4.			Groundwater Quality    		(page 3 of  3)

Site:Waste Water Treatment Plant    			Well Number: OR-0668 (Floridan)

Hydrologist: RBrooks	                                                Casing Depth: 1490 ft

| LAB ( | Date/Time (yy:mm:dd/hh:mm) | Sample Depth (ft, bls) | Open Hole (ft) | Temp (Deg C) | Chlorides (mg/L) | Conductivity (us/cm) |
| --- | --- | --- | --- | --- | --- | --- |
|  | 980430-NA | 1712 | 1108 | NR | 6250 | 18500 |
|  | 980501-1125 | 1743 | 1139 | 27 | 5680 | 19821 |
|  | 980505-1610 | 1775 | 1171 | 25 | 6360 | 17510 |
|  | 980505-1205 | 1808 | 1204 | 26 | 6290 | 19178 |
|  | 980505-1609 | 1839 | 1235 | 25 | 6860 | 17510 |
|  | 980506-2030 | 1870 | 1266 | NR | 14200* | 17510 |
| ( | 980507-1550 | 1900 | 1296 | 28 | 18000 | 39889 |
|  | 980512-1410 | 1,965 | 1,361 | 29 | 21,500 | 44,600 |
|  | 980513-0730 | 1,995 | 1,391 | NR | NR | 43,600 |
|  | 980513-1615 | 2,027 | 1,423 | 27 | 15,700 | 34,600 |
|  | 980514-1120 | 2,058 | 1,454 | 26.5 | 25,800 | 43,700 |
|  | 980514-1700 | 2,089 | 1,485 | NR | 23,500 | 40,500 |
|  | 980515-1300 | 2,120 | 1,516 | 26.5 | NR | 37,400 |
|  | 980518-NR | 2,150 | 1,546 | NR | 12,300 | 35,000 |
|  | 980518-NR | 2,180 | 1,576 | NR | 12,000 | 34,300 |
|  | 980519-NR | 2,215 | 1,611 | 28 | 12,000 | 34,800 |
|  | 980520-NR | 2,245 | 1,641 | NR | NR | 33,700 |
|  | 980521-1050 | 2,310 | 1,706 | 27 | 13,800 | 35,500 |
|  | 980521-1425 | 2,341 | 1,737 | 28 | 12,000 | 35,700 |
|  | 980521- NR | 2,372 | 1,768 | NR | NR | 33,600 |
|  | 980526-1210 | 2,403 | 1,799 | 26 | 13,600 | 41,200 |
|  | 980602-NR | 2,430 | 1831 | NR | NR | 45,500 |
|  | 980603-NR | 2,470 | 1,866 | 26 | NR | 47,500 |
|  | 980603/2200 | 2,498 | 1894 | NR | NR | 42,800 |

Table 5.		Downhole Samples Groundwater Quality

Site:Waste Water Treatment Plant    			Well Number: OR-0668 (Floridan)

Hydrologist: RBrooks

| LAB ( | Date/Time (yy:mm:dd/hh:mm) | Sample Depth (ft, bls) | Open Hole (ft) | Temp (Deg C) | Chlorides (mg/L) | Conductivity (us/cm) |
| --- | --- | --- | --- | --- | --- | --- |
|  | 980307/NR | 600 | 403 | NR | 9.0 | 295 |
|  | 980307/NR | 420 | 223 | NR | 10.0 | 200 |
|  | 980307/NR | 83 | 114 | NR | 7.9 | 338 |
|  | 980413/NR | 1365 | 763 | NR | 210 | 626 |
|  | 980413/NR | 1310 | 708 | NR | 63 | 307 |
|  | 980626/1215 | 2018 | 1416 | NR | 17,000 | 41,000 |
|  | 980626/1315 | 1320 | 718 | NR | 29 | 372 |
|  | 980626/1415 | 1365 | 763 | NR | 9,300 | 24,000 |
| ( | *981130/1525 | 1530 | 40 | NR | 7,888 | 21,590 |

*Sampled after well completion and after well development.

Lithologic Description		(page 1 of 5)

Site: Waste Water Treatment Plant East		Well ID: OR-0668 (Floridan)

Samples Described By: R Brooks, *J Sego

| From (ft) | To (ft) | Lithology |
| --- | --- | --- |
| 0 | 40 | No sample |
| 40 | 55 | Sand, brown, fine to medium |
| 55 | 95 | Sand, brown, silty to very fine |
| 95 | 130 | Sand and shell, olive, silty to very fine (drill bit had clay, green, stiff, minor shell inclusion) |
| 130 | 160 | Clay, dark green |
| 160 | 195 | Dolomite, brown, yellowish gray to gray, cherty, phosphatic |
| 195 | 250 | Limestone, yellowish gray, Leps |
| 250 | 279 | Limestone, yellowish gray, dictyconus and echinoids |
| 279 | 280 | Clay, gray |
| 280 | 312 | Limestone, yellowish gray, soft, dictyconus |
| 312 | 320 | Limestone, dolomitic, light tan, dictyconus, small layer of dolomite at 315 ft. |
| 320 | 325 | Limestone, dolomitic, light tan, dictyconus, small layers of dolomite, olive, hard |
| 325 | 342 | Limestone, dolomitic, light tan, soft, dictyconus abundant |
| 342 | 350 | Limestone, yellowish gray, soft, minor peat |
| 350 | 352 | Limestone, dolomitic, light tan, soft, dictyconus abundant |
| 352 | 374 | Limestone, yellowish gray, very soft, dictyconus and echinoids |
| 374 | 400 | Limestone and Limestone, dolomitic, yellowish gray to tan, soft to medium, dictyconus and echinoids |
| 400 | 403 | Dolomite, tan, hard, minor peat, some secondary porosity |
| 403 | 420 | Limestone, dolomitic, tan to gray, dictyconus |
| 420 | 440 | Dolomite, tan, hard, good secondary porosity in areas, minor peat, (dredging zone 432-434 ft.) |
| 440 | 450 | Dolomite, tan, medium |
| 450 | 460 | Limestone, dolomitic, yellowish gray, soft, dictyconus |
| 460 | 474 | Dolomite, brown, hard, minor secondary porosity |
| 474 | 480 | Limestone, yellowish gray, soft, dictyconus |
| 480 | 500 | Dolomite, dark brown, hard, minor secondary porosity |
| 500 | 520 | Dolomite, dark brown to brown (minor gray), hard, peaty, minor secondary porosity |
| 520 | 530 | Dolomite, dark olive, very hard |
| 530 | 570 | Dolomite, dark brown, very hard, peaty |
| 570 | 610 | Limestone, dolomitic, brown to tan, soft to medium |
| 610 | 630 | Limestone, dolomitic, grayish brown, soft to medium |

Lithologic Description		(page 2 of 5)

Site: Waste Water Treatment Plant East		Well ID: OR-0668 (Floridan)

Samples Described By: R Brooks

| From (ft) | To (ft) | Lithology |
| --- | --- | --- |
| 630 | 750 | Limestone, dolomitic, yellowish brown, pin point porosity, medium |
| 750 | 760 | Limestone, dolomitic, yellowish brown, semi-porous, medium |
| 760 | 770 | Limestone, dolomitic, yellowish brown, silty, pin point porosity, medium |
| 770 | 780 | Limestone, dolomitic, yellowish brown, silty, pin point porosity, minor peat, medium |
| 780 | 800 | Limestone, dolomitic, light yellowish brown, semi-porous, medium |
| 800 | 850 | Limestone, dolomitic, light yellowish brown, pin point porosity, medium |
| 850 | 870 | Dolomite and Limestone, dolomitic, yellowish brown, small vugs, medium |
| 870 | 920 | Limestone, dolomitic, yellowish brown, semi-porous, medium |
| 920 | 930 | Limestone, dolomitic, light yellowish brown, semi-porous, soft to medium |
| 930 | 1010 | Limestone, dolomitic, yellowish brown, semi-porous, soft to medium |
| 1010 | 1020 | Limestone, dolomitic, yellowish gray, no visible porosity, medium |
| 1020 | 1030 | Limestone, dolomitic, yellowish brown, pin point porosity, medium, small layer of gray Limestone, dolomitic |
| 1030 | 1040 | Limestone, dolomitic, light yellowish brown, pin point porosity, medium, peat at 1032-1035 |
| 1040 | 1050 | Limestone, dolomitic, dark brown, very peaty, white geode quartz, medium |
| 1050 | 1060 | Dolomite, yellowish brown, hard |
| 1060 | 1070 | Limestone, dolomitic, light yellowish brown, very small vugs, medium |
| 1070 | 1080 | Limestone, dolomitic, light yellowish brown, semi-porous, medium |
| 1080 | 1090 | Limestone, dolomitic, light yellowish brown, pin point porosity, medium |
| 1090 | 1110 | Dolomite, yellowish brown, pin point porosity, hard |
| 1110 | 1112 | Dolomite, olive, pin point porosity, hard |
| 1112 | 1120 | Dolomite, yellowish gray, some secondary porosity, hard |
| 1120 | 1130 | Dolomite, yellowish brown, some secondary porosity, fine peat layers, hard |
| 1130 | 1140 | Limestone, dolomitic, very light yellowish brown, pin point porosity, minor peat, medium |
| 1140 | 1150 | Limestone, dolomitic, yellowish brown, primary porosity, soft, with small layers of dolomite, pin point porosity, hard |
| 1150 | 1152 | Dolomite, olive, secondary porosity, hard |
| 1152 | 1160 | Dolomite, yellowish brown, no visible porosity, hard |
| 1160 | 1170 | Dolomite, brown, no visible porosity, hard |
| 1170 | 1190 | Dolomite, yellowish brown, secondary porosity, peaty, hard |
| 1190 | 1200 | Dolomite, light yellowish brown and gray, no visible porosity, hard |
| 1200 | 1210 | Limestone, dolomitic, grayish brown, very small vugs, medium |

Lithologic Description		(page 3 of 5)

Site: Waste Water Treatment Plant East		Well ID: OR-0668 (Floridan)

Samples Described By: R Brooks

| From (ft) | To (ft) | Lithology |
| --- | --- | --- |
| 1210 | 1220 | Limestone, dolomitic, yellowish brown, small vugs, minor peat, medium |
| 1220 | 1240 | Dolomite, yellowish brown to olive, no visible porosity, hard with small layers of Limestone, dolomitic |
| 1240 | 1250 | Limestone, dolomitic, yellowish brown, sucrosic, remnant fossils (echinoids), gray inclusions, (dolomitized shell bed), medium |
| 1250 | 1270 | As above, more dolomitized, light yellowish brown, hard, pebble size cuttings |
| 1270 | 1280 | Limestone, dolomitic, dark yellowish brown, more porous than above, dolomitized shell bed as above, medium |
| 1280 | 1290 | Limestone, dolomitic, yellowish brown, primary porosity, sucrosic, medium |
| 1290 | 1310 | As above, soft to medium |
| *1310 | 1395 | Dolomite, olive to dark brown and gray, no visible porosity, minor chert, very hard |
| *1395 | 1490 | Dolomite, brown, hard, sucrosic to cherty, moldic porosity; with dolomite, gray, exhibiting sulfide and/or other inclusions throughout, gypsum crystals at 1435, trace peat at 1455, cobble size cuttings at 1490 |
| *1490 | 1505 | Dolomite, brown, hard; with Limestone, dolomitic, tan-gray, sulfide and/or other inclusions throughout, and some gypsum, peat at 1490 |
| *1505 | 1510 | Dolomite and limestone, dolomitic, soft, trace gypsum, sand sized cuttings |
| *1510 | 1561 | Dolomite, brown hard; with limestone, dolomitic and trace gypsum |
| *1561 | 1566 | Dolomite, brown hard; with limestone, dolomitic and gypsum |
| *1566 | 1578 | Dolomite, brown, hard; with limestone, dolomitic, pin point porosity, little/no gypsum |
| *1578 | 1578 | Dolomite, tan hard; gypsiferous, fossiliferous (echinoids) |
| *1578 | 1581 | SAA; w/clay, gray, and limestone, white, chalky |
| *1581 | 1588 | Dolomite, tan hard; gypsiferous, fossiliferous, cuttings sand to silt sized |
| *1588 | 1617 | Dolomite, brown hard, and limestone, tan, peat at 1592 and gypsum at 1600 |
| *1617 | 1650 | Dolomite, brown hard, and limestone, tan, sand sized material, fossiliferous (valvulina?, dictyconus (very elongate for dictyconus), trends to limestone, dolomitic, brown-gray, and limestone, tan |
| *1650 | 1671 | Limestone, creme colored, and limestone, dolomitic, tan, coming up as fine grained material |
| *1671 | 1720 | Dolomite, brown, and limestone, dolomitic, gray, and limestone, tan with dictyconus |

Lithologic Description		(page 4 of 5)

Site: Waste Water Treatment Plant East		Well ID: OR-0668 (Floridan)

Samples Described By: R Brooks, *J Sego

| From (ft) | To (ft) | Lithology |
| --- | --- | --- |
| *1720 | 1840 | Limestone, dolomitic, tan, pinpoint porosity, fossiliferous dictyconus at 1742 ft |
| *1840 | 1870 | Dolomite, brown, and limestone, tan, soft, sand sized and finer material coming out of discharge line |
| *1870 | 1881 | Dolomite, brown, hard, moldic porosity, fine grained discharge material |
| *1881 | 1890 | Dolomite, brown-gray, hard cherty |
| *1890 | 1910 | Dolomite, tan-brown, sucrosic to cherty, hard; with intermittent gray fine silt clay in suspension |
| *1910 | 1920 | Dolomite, light brown to brown, hard, no visible porosity, cuttings coarse sand size |
| *1920 | 1940 | Dolomite, tan to olive brown, very hard, no visible porosity, cuttings pebble size |
| 1940 | 1950 | SAA, fine pebble size |
| 1950 | 1960 | Dolomite, tan to olive brown, very hard, no visible porosity, cuttings pebble size |
| 1960 | 1970 | Dolomite, light brown to brown, hard, no visible porosity, cuttings coarse sand size |
| 1970 | 1980 | Dolomite, olive brown, medium, cuttings medium sand size |
| 1980 | 1990 | SAA, tan to olive brown, fine |
| 1990 | 2000 | Dolomite, tan to olive brown, very hard, no visible porosity, cuttings fine pebble size |
| 2000 | 2020 | Dolomite, gray to olive brown, very hard, no visible porosity, cuttings fine pebble size |
| 2020 | 2060 | Dolomite, dark gray to tan, very hard, no visible porosity, cuttings fine pebble size |
| 2060 | 2070 | Dolomite, light tanish gray, medium, cuttings fine to medium sand size |
| 2070 | 2110 | Dolomite, olive brown, very hard, no visible porosity |
| 2110 | 2120 | Dolomite, light brown, medium, cuttings medium sand size |
| 2120 | 2130 | Limestone, dolomitic, light brown, soft to medium, cuttings fine sand size |
| 2130 | 2140 | Limestone, dolomitic, brown, medium, silty, semi-porous, cuttings coarse pebble size |
| 2140 | 2150 | Limestone, dolomitic, grayish brown, medium to hard, semi-porous, pebble size, minor dolomite |
| 2150 | 2170 | Limestone, dolomitic, olive brown, medium, cuttings coarse sand size |

Lithologic Description		(page 5 of 5)

Site: Waste Water Treatment Plant East		Well ID: OR-0668 (Floridan)

Samples Described By: R Brooks, *J Sego

| From (ft) | To (ft) | Lithology |
| --- | --- | --- |
| 2170 | 2180 | Limestone, dolomitic, gray, medium, semi-porous, cobble size cuttings |
| 2180 | 2240 | Limestone, dolomitic, brown to gray, medium to hard |
| 2230 | 2280 | Limestone, dolomitic, brown, medium, semi-porous, gypsum (~1%), coarse pebble size cuttings |
| 2280 | 2290 | SAA, less porous |
| 2290 | 2310 | Limestone, dolomitic, gray, soft to medium, silty, gypsum ~ < 1% |
| 2310 | 2340 | Limestone, dolomitic, gray, micritic, soft, gypsum nodules, poor induration, cuttings silty |
| 2340 | 2360 | Limestone, dolomitic, gray, micritic, soft, gypsum nodules, good induration, cuttings silty |
| 2360 | 2380 | Limestone, dolomitic, grayish brown, micritic, soft, gypsum nodules, good induration, cuttings silty |
| 2380 | 2390 | SAA, medium, ~ 20% gypsum |
| 2390 | 2400 | SAA, ~ 50% gypsum |
| 2400 | 2460 | Limestone, dolomitic, gray, soft, silty to fine cuttings, gypsum |
| 2460 | 2470 | Gypsiferous siltstone, very light gray, soft |
| 2470 | 2498 | Limestone, dolomitic, gray, soft, silty to fine cuttings, gypsum |

# Text boxes

12 in. diameter bore

6 in. dia. borehole

Locking steel protective

casing with 4 bollards

LSD (est. @ 80 ft. NGVD)

30 in. dia. Steel Casing

24 in. dia. Steel Casing

18 in. dia. Steel Casing

12 in. dia. Steel Casing

6 in dia. PVC Well casing

3 rubber catch baskets with bentonite hole plug at 1489 ft, 1486 ft and 1433 ft bls

Open Hole

Steel tremie pipe ~ 1,780 - 2,245

Legend

*Grout

*Gravel

* See Grout Table

NOT TO SCALE

3 ft. x 3 ft. Concrete Pad with SJRWD Survey Marker

Unconsolidated sands, clays and shells

34 ft bls

125 ft bls

197 ft bls

602 ft bls

Carbonates

1490 ft bls

1537 ft bls

2498 ft bls

SR 434 (Alafya Trail)

Steel culverts

OR-0664

125 ft X 125 ft site

Ditch

OR-0678

OR-0668

OR-0676

Discharge

lines

Paved Rd

Entrance 2.2 miles to site

Gravel Rd

Powerlines

Retention

ponds

Waste water treatment plant

30 ft ft

10 ft

60 ft

40 ft

OR-0665

N